## Slide 1: Update on BRSKI-AE – Support for asynchronous enrollment
draft-ietf-anima-brski-async-enroll-00
Steffen Fries, Hendrik Brockhaus, Elliot Lear
IETF 109 – ANIMA Working Group

## Slide 2: Recall: Problem statement & Overview
There exists various industrial scenarios, which have limited online connectivity to local or backend services either technically or by policy used during onboarding / enrollment.
  Use Case 1: limited on-site PKI functionality support, requires relying on a backend PKI, to perform (final) authorization of certification requests for operational certificate (LDevID).
  Use Case 2: reversed client – sever roles in deployment or limited connectivity to a domain registrar
Draft addresses these issues by updating BRSKI to support authenticated self-contained objects (signed-wrapped objects) for the certificate enrolment to bind proof of possession and poof of identity to the objects in a similar way as already applied for the voucher handling to be transport independent.

## Slide 3: Current focus on use case 2
Develop interaction between pledge, pledge-agent, and domain registrar
Protocol approach for the first step close to BRSKI, with the specifics of reversed roles between pledge-agent and pledge:
  TLS between components
  HTTP transport of objects
Clarification ongoing on
  Trust relations between components to ensure onboarding of the right pledge in the right domain
  Endpoints for the pledge
  Object format for exchange of signature wrapped objects
+------------------------+
+--------------Drop Ship---------------| Vendor Service |
| +------------------------+
| | M anufacturer| |
| | A uthorized |Ownership|
| | S igning |Tracker |
| | A uthority | |
| +--------------+---------+
| ^
| | BRSKI-
V | MASA
+-------+ +-------+ .............................|.........
| | | | . | .
| | | | . +-----------+ +-----v-----+ .
| | |Pledge | . | | | | .
|Pledge | | Agent | . | Join | | Domain | .
| | | | . | Proxy | | Registrar | .
| <----->.......<-------->...........<-------> (PKI RA) | .
| | | | . | BRSKI-AE | | .
| | | | . | | +-----+-----+ .
|IDevID | |opt. | . +-----------+ e.g. RFC7030 .
| | |IDevID | . +-----------------+------+ .
| | |or | . | Key Infrastructure | .
| | |LDevID | . | (e.g., PKI Certificate | .
+-------+ +-------+ . | Authority) | .
. +------------------------+ .
.......................................
"Domain" components

## Slide 4: BRSKI design team discussions focus on Use case 2: Trust relations
Clarification of trust relation between pledge-agent and pledge and pledge-agent and domain registrar. Ideal: less trust assumptions on pledge-agent.
Options
  Pledge-agent / pledge: Potential use of a QR code or similar to show proximity between pledge and pledge-agent. Can be used for instance in a TLS cipher suite utilizing the QR code. Use of subcerts draft has been discussed, but neglected, as other use cases may not consider a TLS connection here and benefit a close binding (e.g., when using BT or NFC or other)
  Pledge-agent / registrar: Potential use of server side only TLS and HTTP authentication from the pledge-agent (e.g. allowing a service technician to authenticate) as alternative to LDevID on pledge-agent (both already stated in the 00 draft for use case 2)
Ongoing discussion about potential attack and misuse cases when relying on signature wrapped object exchange between pledge and domain registrar

## Slide 5: Further discussions on use case 2: Pledge-endpoints
Endpoints on the pledge are currently discussed allowing a pledge agent to trigger voucher request generation and certification request generation.
Demand seen for at least four endpoints:
  /triggervoucherrequest: initiates request creation on pledge, returns voucher request
  /triggercertrequest: initiates request creation on pledge, returns certification request
  /supplyvoucher: provide voucher to pledge, returns voucher status
  /supplycertificate: provide certificate (and cain) to pledge, returns certificate confirmation
Clarification has to start regarding supported encodings of the objects exchanged:
  Current voucher object is CMC-signed-JSON. Discussion on relying on JWS-signed-JSON in the first step, would also align with using similar formats for the certification request.

## Slide 6: Changes to IETF draft 00 (not submitted yet)
Update of scope in Section 3.1 to include that specifically in the pledge acts as a server in use case 2.
Update of introduction of use case 2 in Section 5.2 to state that the transport between the pledge and the pledge agent will be HTTP in the context of this document but may also be done using other protocols. Introduction of sub section related to the discovery of pledge and pledge-agent in use case 2 in Section 5.2.4
Clarification in discovery options for enrollment endpoints at the domain registrar based on well-known endpoints in Section 5.3. Note that the change to /brski for the voucher related endpoints has been taken over in the BRSKI main document.
Updated references.

## Slide 7: Discussion, open issues from IETF 108
#1 Discovery of enrollment options on registrar: uses “GET / .well-known/” resulting in the enumeration of available endpoints on the domain registrar, so pledge or pledge-agent may pick
#2 Pledge-agent authentication and authorization in use case 2 towards domain registrar  ongoing discussion in design team
#3 Necessity of providing (proximity) registrar certificate to pledge for inclusion into voucher request: current discussion in design team tends to support this to enable registrar to verify that he is the target registrar
#4 Consideration of different transport options in the addressing scheme for the enrollment protocol: current draft assumed to follow the BRSKI approach (HTTP)

## Slide 8: Next Steps
Further refinement of the approach in the design team
Circulate outcome on the mailing list for further discussion
Update draft with results