## Slide 1: BRSKI with Pledge in Responder Mode (BRSKI-PRM)
draft-ietf-anima-brski-prm-04
Repo URL: https://github.com/anima-wg/anima-brski-prm
Steffen Fries, Thomas Werner, Elliot Lear, Michael Richardson
IETF 114 – ANIMA Working Group

## Slide 2: BRSKI-PRM Status History of main changes 0203
Mostly editorial improvements based on review comments
Updated examples to state "base64encodedvalue==" for x5c occurrences
Include link to SVG graphic as general overview
Restructuring of section 5 to flatten hierarchy
Enhanced requirements and motivation in Section 4
7/8/2022
2

## Slide 3: BRSKI-PRM Status History of main changes 0304
Peer review done by Esko Dijk (issues #22-#61)
Majority of issues targets to improve and clarify the current description to avid ambiguities. Technical issues are also contained
Added support for nonceless voucher, issue #18
  Allows for provisioning of voucher via the sales channel
Defined pledge-CAcerts endpoint and usage, issue #21
  Handling of providing a wrapped CA certs response to the pledge in section Section 5.5.3; also added new required registrar endpoint (section Section 5.5.2 and IANA considerations) for the registrar to provide a wrapped CA certs response, issue #21
PoP registrar certificate as mandatory, issue #
Added clarification that registrar-agent may collect PVR or PER or both in one run, issue #17
7/8/2022
3

## Slide 4: BRSKI-PRM Status History of main changes 0304 (cont.)
SKID format clarified to be just the octects of the SKID, without any ASN.1 information
Simplified YANG definition by augmenting the voucher request from RFC 8995 instead of redefining it.
Added explanation for terminology "endpoint" used in this document, issue #16
Removed join proxy in Figure 1 and added explanatory text, issue #20
7/8/2022
4

## Slide 5: BRSKI-PRM Status Next Steps
Currently 14 open issues, which will be addressed after IETF 114. All of them target improvement of the approach by clarifying handling/response codes/endpoints.
Security consideration section to be updated
PoC implementation finished
Interop testing with others welcome
Document shepherd needed
After addressing the remaining open issues ready for WGLC
7/8/2022
5

## Slide 6: Backup
6

## Slide 7: BRSKI-PRM – Abstract Protocol Overview
7/8/2022
7
Trigger Voucher-request { {reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Verification of “agent-signed-cert” and “agent-signed-data”
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}, signed
Basement no connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
RA
Domain CA
MASA
Trigger Enrollment-request
Enrollment-request {signature-wrapped CSR}
Voucher {reg-cert, assertion, …}, signed
Voucher-status
Enrollment-response {LDevID cert}
Enrollment-status
Enrollment-request (CSR)-request
Enrollment-response (LDevID cert)
IDevID
Manufacturer trust anchor
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher and LDevID cert to pledge
First floor, connectivity to backend
Device audit log
Voucher status
Enrollment status
Provisional accept of registrar certificate