## Slide 1: Update on BRSKI-AE – Support for asynchronous enrollment
draft-ietf-anima-brski-async-enroll-04
Steffen Fries, Hendrik Brockhaus, Elliot Lear, David von Oheimb
BRSKI with Pledge in Responder Mode (BRSKI-PRM)
draft-ietf-anima-brski-prm-00
Steffen Fries, Thomas Werner, Elliot Lear, Michael Richardson
Steffen Fries
IETF 112 – ANIMA Working Group

## Slide 2: Discussion on draft split
Original BRSKI-AE discussed two use cases, which have evolved into different directions
Discussion (ANIMA Design Team, mailing list) to split the draft along the two use cases
UC1 stays as "Support of Asynchronous Enrollment in BRSKI (BRSKI-AE)" covering the application of alternative enrollment protocols. It will cover the description of utilizing other enrollment protocol than EST /simpleenroll in general and using Lightweight CMP specifically. Focus is the interaction between pledge and registrar.
UC2 became "BRSKI with Pledge in Responder Mode (BRSKI- PRM)", and addresses the communication between the pledge and the registrar by reversing the initiator and responder role (compared to RFC 8995) introducing a registrar-agent component to facilitate the communication.
11/10/2021
2

## Slide 3: BRSKI-AE Status History of changes
From version 02 to version 03
  Housekeeping, deleted open issue regarding YANG voucher-request in UC2 as ietf-voucher-request was enhanced with additional leaf.
  Included open issues of Voucher YANG model in UC2 regarding assertion value agent-proximity and CSR encapsulation using SZTP sub module.
From version 03 to version 04
  Moved UC2 related parts defining pledge in responder mode to BRSKI-PRM (#19).
  Updated references to the Lightweight CMP Profile.
  Change of authors: Added David von Oheimb as co-author. Thomas Werner left.
11/10/2021
3

## Slide 4: BRSKI-AE Next Steps
Clarification of open issues stated in the draft (currently no open issues on ANIMA git)
Further update general description using alternative enrollment protocols and the concrete examples
  Lightweight CMP Profile
  EST with /fullCMC
Updates will be circulated
WG review appreciated
PoC implementation ongoing  Interest from others welcome for interop testing
11/10/2021
4

## Slide 5: BRSKI-PRM Status History of changes from BRSKI-AE-03 to BRSKI-PRM-00
Moved UC2 defining pledge in responder mode from BRSKI-AE-03 to BRSKI-PRM-00.
Yang doctor early review addressed (ietf-voucher-request enhancements (Section 6, Security Considerations Section).
Aligned naming of ietf-voucher-request-xxx with other ANIMA drafts (#20).
Utilized ietf-voucher-request-prm in voucher exchanges (to use enhancements for agent-signed-data).
Included changes from draft-ietf-netconf-sztp-csr-06 regarding the YANG definition of csr-types into the enrollment request exchange.
11/10/2021
5

## Slide 6: BRSKI-PRM Status Next Steps
Further rework the draft (structure and application examples)
Clarification of open issues stated in ANIMA git and also in the draft
  Verification of usage of ietf-ztp-types to convey PKCS#10 in BRSKI-PRM enrollment request (#5)
  Option to generate multiple CSRs (domain specific, application specific) (#7)
  Signature on enrollment response object? Protection of additional data contained or identification of registrar providing the certificate (audit) (#8)
Circulate outcome on the mailing list for further discussion
WG review appreciated
PoC implementation ongoing  Interest from others welcome for interop testing
11/10/2021
6

## Slide 7: Backup
7

## Slide 8: BRSKI-AE Abstract Protocol Overview
Voucher-request {S/N, reg-cert, …}
S/N verification
Verification of plege signature and IDevID (pledge)
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Issues voucher with assertion proximity
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Pledge (caller)
Domain Registrar
Domain CA
MASA
Certification-request
Certification-response (LDevID Cert)
IDevID
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
8
Step1: Voucher request/response handling as in BRSKI
Step2: Application of alternative enrollment protocol, (e.g. Lightweight-CMP)
Request CA certificates (opt.)
CA certificates (opt.)
Request certificate attributes (opt.)
Certificate attributes (opt.)
Verification of LDevID Cert
Verification of IDevID Cert
Voucher-status
Enrollment-status

## Slide 9: BRSKI-PRM Abstract Protocol Overview
Trigger Voucher-request { {reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Basement no connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
Domain CA
MASA
Trigger Enrollment-request
Enrollment-request {signature-wrapped CSR}
Voucher {reg-cert, assertion, …}
Voucher-status
Enrollment-response {LDevID Cert}
Enrollment-status
Enrollment-request (CSR)-request
Enrollment-response (LDevID Cert)
IDevID
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
9
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher and LDEvID cert to pledge
First floor, connectivity to backend

## Slide 10: Original drawings (just used them as picture as they better scale)
10
Voucher
Request
SN: 1234
Assertion:
proximity
SN: 1234
2021-04-16
Voucher
Request
SN: 1234
Assertion:
proximity
SN: 1234
2021-04-16
Voucher request
Cert
Request
CR
IDevID
BRSKI-PRM
BRSKI-AE
Voucher
Request
SN: 1234
Assertion:
proximity
SN: 1234
2021-04-16
Voucher request
Voucher
Request
SN: 1234
LDevID EE (Reg)
Assertion:
agent-proximity
SN: 1234
2021-04-16
Enroll
Request
IDevID
CSR